N447RV

Van’s Aircraft RV-7A

Experimental

Pilot Operating Handbook

WARNING

The aircraft described in this handbook is amateur built and certified in the Experimental category.  While believed to be complete and accurate at the time of publication/revision, this handbook may not contain all of the information necessary for the pilot to safely operate the aircraft.  It is also not a substitute for competent flight and/or aerobatic instruction.  The Pilot in Command alone is responsible for ensuring the initial and continuing airworthiness of this aircraft and for its operation within the limits detailed herein.  All persons entering this aircraft do so at their own risk.

HISTORY

Van’s Aircraft was founded in 1973 by Richard VanGrunsven, an engineer and former Air Force officer.  Van’s first offering was the RV-3, a single-seat sport kit plane that conquered the hearts of many.  Soon after, in 1979, the RV-4 followed, answering the demand for a two-seater version of the RV-3.  Dick gave the RV-4 a tandem seating arrangement to maintain centerline view and keep a low aerodynamic profile.  Next out of the drawing board came the RV-6, which was a side-by-side, two-seater and first flew in 1985?  This was the first Van’s aircraft to also be available in a tricycle landing gear configuration, called the RV-6A.  The RV-6 went on to become the most successful kit plane in history, with flying kit numbers approaching 2000 today.

After the RV-6, Dick designed the RV-8/8A and the RV-9/9A.  They flew in 1995 and 1997, respectively.  The RV-8/8A was a re-visit to the tandem concept, and the first Van’s design to make use of CAD (Computer Aided Design).  One of the big advantages of this was that the Van’s Aircraft kits were now much easier to build with most of the parts being pre-punched and a new option was added, the Quick Build kit.  Next in line was the RV-7/7A, being introduced in the spring of 2001.  As of this writing there are nearly 200 RV-7 kit flying.

Dick received many requests for a plane similar to his RV-6 in performance, but with more range, more useful load, and room for a bigger engine.  Out came the RV-7 and RV-7A.  It also adds more legroom and headroom to the original RV-6 design, while maintaining the same maneuverability and near-STOL performance.  It has some parts in common with the RV-8/8A and RV-9/9A, and accepts Lycoming engines from 150-200 hp.  Quoting Van’s, “…the RV-7/7A is everything the RV-6/6A was (and is) plus more room, better visibility, more load, more range, more engine options, and a very advanced kit”.

# GENERAL

## MANUFACTURER & BUILDER INFORMATION

| Kit Manufacturer and Model: | Van’s Aircraft RV-7A |
| --- | --- |
| Serial Number: | 71266 |
| Aircraft Registration Number: | N447RV |
| Maiden Flight: | 08/13/2005 |
| Builders: | Walter H. Tondu Lawrence W. Tondu |
| Owner: | Walter H. Tondu |

## VIEWS

## AIRFRAME SPECIFICATIONS

| Wing Span: | 25 ft. 0 in. |
| --- | --- |
| Length: | 20 ft. 4 in. |
| Height: | 7 ft. 10 in. |
| Cabin Height: | 42 in. |
| Cabin Width: | 43 in. |
| Cabin Length: | 51 in. |
| Baggage Area: | 12+ cu. Ft. |
| Wing Area: | 121 sq. ft. |
| Wing Loading: | 14.8 lb./sq. ft. |
| Main Gear Track: | 91 in. |
| Flap Travel: | 40 deg. |
| Aileron Travel: | 32 deg. Up / 17 deg. Down |
| Elevator Travel: | 30 deg. Up / 25 deg. Down |
| Rudder Travel: | 35 deg. Left / 35 deg. Right |
| Nose Gear Breakout Force: | 22 lbs. |
| Tail Group Airfoil: |  |
| Horizontal Stabilizer Span: |  |
| Horizontal Stabilizer Incidence: |  |

## PERFORMANCE SPECIFICATIONS

| Speed: |  |  |
| --- | --- | --- |
|  | Maximum at Sea Level |  |
|  | Cruise, 75% Power at 8,000 Ft |  |
| Range (includes 3 gal. for taxi, takeoff & climb): |  |
|  | 75% @ 8000’ , no reserve |  |
|  | 55% @ 8000’ no reserve |  |
|  | 75% @ 8000’, one hour (10 gal) reserve |  |
|  | 55% @ 8000’, one hour (10 gal) reserve |  |
| Rate of Climb at Sea Level: |  |
| Service Ceiling: |  |  |
| Takeoff Performance: |  |
| Landing Performance: |  |
| Stall Speed (CAS): |  |  |
|  | Flaps Up, Power Off |  |
|  | Flaps Down, Power Off |  |
| Maximum Weight (Normal Category): | 1950 Lbs |
| Empty Weight: |  | 1121 Lbs |
| Maximum Useful Load: | 829Lbs |
| Baggage Allowance: | 100 Lbs |
| Wing Loading (Pounds/ Sq. Ft): | 14.8 Lbs |
| Power Loading (Pounds/ HP): | 10 Lbs |
| Fuel: |  |  |
|  | Capacity | 42 Gal Total |
|  | Type | 100 LL |
| Oil Capacity: |  | 8 Qts. |
| Engine: | Fuel Injected | XE-360 |
| Propeller: | Whirlwind | 200RV |

## ENGINE

Manufacturer:		Penn Yan Aero

Type:			XE-360

Fuel Injected

Horizontal Sump

LASAR Ignition

RAM Air

## PROPELLER

Manufacturer:		Whirlwind

Type:			200RV

Pitch Setting:		Constant Speed

Diameter:		72”

## FUEL

Grade:				100LL

Capacity STBD Tank:		20.98 US Gal. Useable

(0.02 gals unusable)

Capacity PORT Tank:		20.97 US Gal. Useable

(0.03 gals unusable)

## OIL

Type:			Lycoming Oil

Capacity:		8 quarts

Ambient Air Temp	Viscosity Grade

Above 60 F		SAE 50*

30 to 90 F		SAE 40*

0 to 70 F		SAE 30*

Below 10 F		SAE 20*

* or suitable multigrade oil

# OPERATING LIMITATIONS

## AIRSPEED LIMITATIONS

|  | SPEED | KIAS | REMARKS |
| --- | --- | --- | --- |
| VNE | Never Exceed Speed | 200 | Do not exceed this speed in any operations. |
| VNO | Maximum Structural Cruising Speed | 167 | Exceed this speed only in smooth air. |
| VA | Maneuvering Speed | 123 | Do not make full control movements above this speed. Full elevator deflection will result in a 6g load at this speed. |
| VFE | Maximum Flap Extended Speed | 86 | Do not exceed this speed with flaps down |
| Vy | Best Rate of Climb | 96 |  |
| Vx | Best Angle of Climb | 70 |  |
| Vs | Stall Speed Clean | 55 |  |
| Vso | Stall Speed Landing Configuration | 50 |  |

### AIRSPEED INDICATOR MARKINGS

| MARKING | KIAS VALUE OR RANGE | SIGNIFICANCE |
| --- | --- | --- |
| White Arc | 50-86 | Full Flap Operating Range. Lower limit is Vso. Upper limit is maximum speed with flaps extended |
| Green Arc | 55-167 | Normal Operating Range. Lower limit is Vs. Upper limit is maximum structural cruising speed |
| Yellow Arc | 167-200 | Operations must be conducted with caution and only in smooth air. |
| Red Line | 200 | Maximum speed for all operations |

### PROPELLER LIMITATIONS

It is recommended to avoid continuous operation of the 200RV propeller in the RPM range between 2050 to 2300 RPM and 2600 to 2700 RPM.

OVERSPEED WARNING

It is possible to over speed the propeller by rapid throttle advancement.  Therefore, always adjust the power and RPM lever slowly and smoothly to avoid the possibility of over speed.  If an over speed occurs:

| Over speed Occurrence | Required Action |
| --- | --- |
| Up to 110 % of the max RPM | A 50 hours inspection must be performed immediately. |
| 111% to 120% of the max RPM | A mandatory teardown inspection at the factory is required |
| Above 121% of the max RPM | No further use of the propeller is permitted! The propeller must be returned to the factory for inspection |

WARNING:  Failure to adhere to these guidelines may lead to a catastrophic propeller structural failure.  Any type of structural failure may result in death or sever bodily injury.

## PERMITTED MANEUVERS

### NORMAL OPERATIONS

Normal operations up to maximum take-off weight (as stated in section 6) are limited to normal flying maneuvers, but may include straight and steady stalls and turns in which the bank angle does not exceed 60 degrees.

Spins are permitted.

### APPROVED AEROBATIC MANEUVERS

Aerobatic Maneuvers are permitted within the following limitations:

Aircraft Weight not to exceed 1600 lbs.

G limits are +6/-3

Aft of C.G. limit not to exceed 84.5” aft of datum, where datum is 70” forward of wing leading edge.

#### RECOMMENDED ENTRY SPEEDS

| Maneuver | Entry Speed Range (K.I.A.S.) |
| --- | --- |
| Loops, Horizontal Eights | 120-165 |
| Immelmans, wingovers | 130-165 |
| Aileron Rolls, Barrel Rolls | 105-165 |
| Vertical Rolls | 155-165 |
| Split-S | 85-95 |

## PROHIBITED MANUVERS

Tail Slides

### MANUVERS NOT RECOMMENDED

Snap Rolls (allowable at entry speeds less than 80 knots, but not recommended).

Negative G Maneuvers (not recommended due to possible engine oil starvation and possible prop over speed.

## CROSSWIND COMPONENT

The maximum demonstrated crosswind component for take-off and landings is XX knots.

## POWER AND TEMPERATURES

## OIL PRESSURE

## OIL TEMPERATURE

## FUEL PRESSURE

# PREFLIGHT CHECKLIST

## CABIN

- POH, A-R-R-O-W – AVAILABLE IN AIRPLANE

- Aeronautical Charts – CURRENT AND APPROPRIATE TO FLIGHT

- All Switches – OFF

- Master Switch – ON

- Fuel Quantity – CHECK QUANTITY

- Flaps – DOWN

- Master Switch – OFF

- Control Lock – REMOVE

## EMPENNAGE

- Tail Tie-Down – DISCONNECT

- Control Lock – REMOVE

- Control Surfaces – CHECK

- Trim Tab – SECURE

- Static Sources (both sides of fuselage) – CHECK for blockage

- Tail and Strobe – CHECK CONDITION

## RIGHT WING

- Right Wing Tank – SUMP

- Fuel Quantity – CHECK VISUALLY

- Fuel Filler Cap – SECURE

- Wing Tie-Down – DISCONNECT

- Main Wheel Tire – CHECK for proper inflation and wear

- Brakes – CHECK for cracks and security

- Chock – REMOVE

- Right Landing Light – CHECK condition

- Nav and Strobe – CHECK condition

- Aileron – CHECK freedom of movement and security

- Flap -- CHECK security

## NOSE

- Engine Oil Level – CHECK, do not operate with less than 6 Qts.

- Cowl Hinge Pins – CHECK for security

- Propeller and Spinner – CHECK for nicks and security

- Engine Air Inlets – CHECK for obstructions

- Filtered Air Inlet – CHECK for restrictions

- Ram Air Inlet – CHECK for restrictions

- Nose Wheel Tire – CHECK for proper inflation and wear

- Chock – REMOVE

- Fuel Tank Vents -- CHECK for blockage

- Cabin Air Intakes – CHECK for blockage

## LEFT WING

- Left Wing Tank – SUMP

- Fuel Quantity – CHECK VISUALLY

- Fuel Filler Cap – SECURE

- Pitot Tube Cover – REMOVE and check for blockage

- Wing Tie-Down – DISCONNECT

- Main Wheel Tire – CHECK for proper inflation and wear

- Brakes – CHECK for cracks and security

- Chock – REMOVE

- Nav and Strobe – CHECK condition

- Aileron – CHECK freedom of movement and security

- Flap -- CHECK security

## PRE-START CHECKLIST

- All Switches – OFF

- Throttle – IDLE

- Propeller – HIGH RPM

- Mixture – CUT-OFF

- Ram Air – OFF

- Flight Controls – CHECK

- Fuel Selector – FULLEST TANK

- Avionics – ON AS NEEDED

- Check Weather – ATIS, FSS

- Transponder – SET

- Request Clearance

- Passenger Briefing – COMPLETE

- Loose Items – STOWED

- Seat Belts and Shoulder Harnesses -- TIGHT

- Canopy – CLOSED OR TAXI POSITION

## STARTING ENGINE (Cold)

- Fuel Selector – FULLEST TANK

- Master Switch – ON

- Left Ignition – ON

- Right Ignition – ON

- EIS – ON

- Throttle – FULL IN

- Mixture – RICH

- Fuel Boost Pump – ON 5 seconds to prime then OFF

- Throttle – IDLE, cracked

- Propeller Area – CLEAR

- Starter – START

- Throttle – ADJUST for 1000 RPM or less

- Oil Pressure – CHECK

- Ammeter – CHECK

- Mixture – LEAN

- Radios/Avionics – ON

- Transponder – STANDBY

- Nav & Strobe – ON

## STARTING ENGINE (Warm)

- Fuel Selector – FULLEST TANK

- Master Switch – ON

- Left Ignition – ON

- Right Ignition – ON

- EIS – ON

- Throttle – FULL IN

- Mixture – IDLE CUT OFF

- Propeller Area – CLEAR

- Starter – START

- Mixture – RICH as engine fires

- Throttle – ADJUST for 1000 RPM or less

- Oil Pressure – CHECK

- Ammeter – CHECK

- Mixture – LEAN

- Radios/Avionics – ON

- Transponder – STANDBY

- Nav & Strobe – ON

## BEFORE TAKE-OFF

- Canopy – CLOSED and LOCKED

- Flaps – UP or AS NEEDED

- Fuel Selector – VERIFY FULLEST TANK

- Elevator Trim – TAKEOFF position

- Aileron Trim – TAKEOFF position

- Throttle – 1800 RPM

- Mixture – LEAN for Max RPM’s at high elevations

- Left Ignition –  CHECK RPM DROP

- Right Ignition – CHECK RPM DROP

- Prop – CYCLE 2-3 TIMES

- Engine Instruments – CHECK

- Strobes – AS NEEDED

- Landing Lights – AS NEEDED

- Ammeter – CHECK

- Throttle –  IDLE

- Flight Instruments – SET

- Transponder – ALT

- Boost Pump – ON

## NORMAL TAKEOFF

- Throttle – FULL

- V1 = 55 KIAS (decision)

- Vr = 60 KIAS (rotate)

- Climb Speed – 110 KIAS

- Boost Pump – OFF above 1000 feet AGL

## SHORT FIELD TAKEOFF

- Wing Flaps – 10 Deg

- Brakes – APPLY

- Throttle – FULL – DO NOT EXCEED 2700 RPM

- Mixture – RICH (above 3000’ lean to obtain max RPM)

- Brakes – RELEASE

- Climb Speed – 85 KIAS

- Boost Pump – OFF above 1000 feet AGL

## ENROUTE CLIMB

- Throttle – 25 in Hg, or full throttle

- Propeller – 2500 RPM

- Mixture – LEAN above 5000 AGL

- Autopilot – CHECK and SET

- Landing Lights – ASS NEEDED

- Airspeed – 110 – 130 KIAS

## LANDING CHECKLIST

- Autopilot – AS NEEDED

- Fuel Selector – FULLEST TANK

- Mixture – RICH

- Fuel Pump – ON

- Seat Belts – SECURE

- Approach speed 80 KIAS

- Flaps – AS NEEDED

- Prop – IN - FULL RPM

- Landing Lights – AS NEEDED

## AFTER LANDING

- Boost Pump – OFF

- Transponder – STANDBY

- Mixture – LEAN

## ENGINE SHUTDOWN

- Throttle – IDLE

- Avionics – OFF

- Lights – OFF

- Electrical Switches – OFF

- Mixture – CUT-OFF

- Fuel Selector – OFF

- Right Ignition – OFF

- Left Ignition – OFF

- Master – OFF

## SECURING AIRCRAFT

- Wheel Chocks

- Wing & Tail Tie-Down

- Pitot Tube Cover

- Cockpit

- Master and Electrical Switches – OFF

- Canopy Locked

# EMERGENCY CHECKLISTS

## AIRSPEEDS FOR EMERGENCY OPERATIONS (KIAS)

| Engine Failure After Takeoff: |  |
| --- | --- |
| Wing Flaps Up: | 78 (sink rate of 1100 fpm) |
| Wing Flaps Down: | 70 (sink rate of 1300 fpm) |
| Maneuvering Speed (Va): | 123 |
| Maximum Glide: | 78 |

## ELECTRICAL / ALTERNATOR FAILURE

- Standby Alternator – ON

- E-Bus Alternate Feed – ON

- Avionics – SHED LOADS AS REQUIRED

- Master Switch – OFF

- Flight – TERMINATE as soon as practical

## ENGINE FAILURE DURING TAKEOFF RUN

- Throttle –IDLE

- Brakes – APPLY

- Wing Flaps – RETRACT

- Mixture – IDLE CUT-OFF

- Ignition Switches – OFF

- Master Switch – OFF

## ENGINE FAILURE IMMEDIATELY AFTER TAKEOFF

- Airspeed – 70 KIAS

- Mixture – IDLE CUT-OFF

- Fuel Selector Valve – OFF

- Ignition Switches – OFF

- Wing Flaps – AS REQUIRED

- Master Switch – OFF

## ENGINE FAILURE DURING FLIGHT

- Airspeed – 78 KIAS

- Boost Pump – ON

- Fuel Selector – SWITCH TANKS

- Mixture – RICH

- Ignition Switch –LEFT, RIGHT ON

- Transponder – 7700

## FIRE DURING START ON GROUND

- Mixture – IDLE CUT-OFF

- Fuel Selector Valve – OFF

- Master Switch – OFF

- Ignition Switches – OFF

- Exit Aircraft and Extinguish Fire

## ENGINE FIRE IN FLIGHT

- Mixture – IDLE CUT-OFF

- Fuel Selector Valve – OFF

- Master Switch – OFF

- Ignition Switches – OFF

- Cabin Heat and Air – OFF

- Airspeed – INCREASE TO EXTINGUISH FIRE

- Land Immediately

## ELECTRICAL FIRE IN FLIGHT

- Master Switch – OFF

- Avionics – OFF

- All Other Switches (except ignition) – OFF

- Vents/ Cabin Air/ Heat – CLOSED

- Fire Extinguisher – ACTIVATE (if available)

- Land Immediately

## CABIN FIRE

- Master Switch – OFF

- Vents/ Cabin Heat – CLOSED

- Fire Extinguisher – ACTIVATE (if available)

## WING FIRE

- Nav & Strobe Lights – OFF

- Landing Light – OFF

## LANDING WITHOUT ENGINE POWER

- Airspeed – 78  FLAPS UP / 70 FLAPS EXTENDED

- Mixture – IDLE CUTOFF

- Fuel – OFF

- Left/Right Ignition – OFF

- Flaps – AS NEEDED

- Master Switch – OFF

- Canopy – UNLOCKED

- Seatbelts – SECURE

## PRECAUTIONARY LANDING WITH ENGINE POWER

- Airspeed – 70

- Mixture – RICH

- Flaps – 20 Deg.

- Selected Field – FLY OVER – NOTE OBSTRUCTIONS

- Electrical Switches – OFF

- Master Switch – OFF

- Canopy – UNLOCKED

- Seatbelts – SECURE

## DITCHING

- Radio – MAYDAY on 121.5

- Transponder – SQUAWK 7700

- Airspeed – 70

- Landing – LEVEL ATTITUDE

# PERFORMANCE

## Cruise Performance

| 8000 ft. |
| --- |
| KTS | RPM | MAP | Fuel Flow | % Power |
|  | 2450 | 23” |  | 75% |
|  | 2350 | 22” |  | 65% |
|  | 2250 | 21” |  | 55% |

## NO WIND RANGE AT 8000 ft.

- All range calculations include 3 gal. for engine start, taxi, takeoff and climb.

- Engine is leaned for best economy.

One hour (XX.X  gal.) reserve:

75% Power ………………………………………………..	XXX  sm

65% Power ………………………………………………..	XXX  sm

55% Power ………………………………………………..	XXX  sm

No Reserve:

75% Power ………………………………………………..	XXX  sm

65% Power ………………………………………………..	XXX  sm

55% Power ………………………………………………..	XXX  sm

## ENGINE OUT GLIDE PERFORMANCE AT 78 KIAS

# WEIGHT AND BALANCE DATA

| Maximum Weights |  |
| --- | --- |
| Aerobatic Category: | 1600 lbs. |
| Utility Category: | 1700 lbs. |
| Normal Category: | 1950 lbs. |

Datum is 70 inches forward of wing leading edge (L.E.).

Design C.G. Range is 78.7” to 86.82” aft of Datum.

Forward CG Limit is 15% of chord or 8.7” aft of L.E.

Aft CG Limit is 29% of chord or 16.82” aft of L.E.

Aerobatic Aft CG Limit is 25% of chord or 14.5” aft of L.E.

Main wheel right is 93.96” aft of datum.

Main wheel left is 93.96” aft of datum.

Nose wheel is 39.11” aft of datum.

Fuel is 80” aft of datum.

Pilot and Passenger are 97.48” aft of datum.

Baggage is 126.78” aft of datum.

## EMPTY WEIGHT CG

Aircraft weighed empty in level flight attitude, includes 8 quarts of oil and no fuel.

C.G = 79.57” aft of datum for Empty Weight CG.

|  | Weight | Arm | Moment |
| --- | --- | --- | --- |
| Right Wheel | 423 | 93.96 | 39745.08 |
| Left Wheel | 404 | 93.96 | 37959.84 |
| Nose Wheel | 294 | 39.11 | 11498.34 |
| Total: | 1121 | 79.57 | 89203.26 |

## SAMPLE WEIGHT AND BALANCE DATA

### SITUATION 1: GROSS WEIGHT CG

|  | Weight | Arm | Moment |
| --- | --- | --- | --- |
| Aircraft | 1121 | 79.57 | 89203.26 |
| Fuel (42 Gal.) | 252 | 80.00 | 20160.00 |
| Pilot | 250 | 97.48 | 24370.00 |
| Passenger | 227 | 97.48 | 22127.96 |
| Baggage | 100 | 126.78 | 12678.00 |
| Total: | 1950 | 86.43 | 168539.22 |
| C.G. = 86.43 in. aft of datum. |

### SITUATION 2: MOST AFT CG - GROSS WEIGHT, MIN. FUEL

|  | Weight | Arm | Moment |
| --- | --- | --- | --- |
| Aircraft | 1121 | 79.57 | 89203.26 |
| Fuel (5 Gal.) | 30 | 80.00 | 2400.00 |
| Pilot | 250 | 97.48 | 24370.00 |
| Passenger | 155 | 97.48 | 15109.40 |
| Baggage | 100 | 126.78 | 12678.00 |
| Total: | 1656 | 86.81 | 143760.66 |
| C.G. = 86.81 in. aft of datum. |

### SITUATION 3: MOST FORWARD CG - STD PILOT, MAX. FUEL

|  | Weight | Arm | Moment |
| --- | --- | --- | --- |
| Aircraft | 1121 | 79.57 | 89203.26 |
| Fuel (42 Gal.) | 252 | 80.00 | 20160.00 |
| Pilot | 185 | 97.48 | 18033.80 |
| Passenger | 0 | 97.48 | 0 |
| Baggage | 0 | 126.78 | 0 |
| Total: | 1558 | 81.77 | 127397.06 |
| C.G. = 81.77 in. aft of datum. |

### SITUATION 4: MOST FORWARD CG - MIN. PILOT, MAX FUEL

|  | Weight | Arm | Moment |
| --- | --- | --- | --- |
| Aircraft | 1121 | 79.57 | 89203.26 |
| Fuel (42 Gal.) | 252 | 80.00 | 20160.00 |
| Pilot | 100 | 97.48 | 9748.00 |
| Passenger | 0 | 97.48 | 0 |
| Baggage | 0 | 126.78 | 0 |
| Total: | 1473 | 80.86 | 119111.26 |
| C.G. = 80.86 in. aft of datum. |

# ENGINE INFORMATION

| Model | Penn Yan XE 360, Fuel Injected, Horizontal Sump |
| --- | --- |
| HP | 180 |
| Fuel | 100LL octane minimum |
| Oil Filter | Champion CH48110 |
| Oil Sump Capacity | 8 U.S. Quarts |
| Minimum Safe Quantity | 4 U.S. Quarts |
| Oil | MIL-L-6082 Ashless Dispersant |

## OIL GRADES

| Ambient Air Temp. | Grades | Grades |
| --- | --- | --- |
| Above 80F | S.A.E. 60 | S.A.E. 60, 20w50 |
| Above 60F | S.A.E. 60 |  |
| 30 – 90F | S.A.E. 40 | S.A.E. 40, 50 |
| 0-70F | S.A.E. 30 | S.A.E. 30, 40 or S.A.E 40 |
| Below 10F | S.A.E. 20 | S.A.E. 30 or 20w30 |

## OPERATING CONDITIONS/LIMITATIONS

|  | Desired | Min | Max |
| --- | --- | --- | --- |
| Oil Inlet Temperature: | 180 F | 100 F | 240 F |
| Oil Pressure: | 25 psi at idle | 55 psi | 95 psi |
| Fuel Pressure: |  |  |  |
| Cylinder Head Temperature: | 350 – 390 F | 150 F | 430 F |
| Max Oil Consumption: |  |  | .45 qts./hr. |

# REFERENCE MATERIAL

## TEMPERATURE CONVERSION CHART

| Celc. | Fahr. | Celc. | Fahr. | Celc. | Fahr. | Celc. | Fahr. | Celc. | Fahr. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 10 | 50 | 60 | 140 | 110 | 230 | 160 | 320 | 210 | 410 |
| 16 | 60 | 66 | 150 | 116 | 240 | 166 | 330 | 216 | 420 |
| 21 | 70 | 71 | 160 | 121 | 250 | 171 | 340 | 221 | 430 |
| 27 | 80 | 77 | 170 | 127 | 260 | 177 | 350 | 227 | 440 |
| 32 | 90 | 82 | 180 | 132 | 270 | 182 | 360 | 232 | 450 |
| 38 | 100 | 88 | 190 | 138 | 280 | 188 | 370 | 238 | 460 |
| 43 | 110 | 93 | 200 | 143 | 290 | 193 | 380 | 243 | 470 |
| 49 | 120 | 99 | 210 | 149 | 300 | 199 | 390 | 249 | 480 |
| 54 | 130 | 104 | 220 | 154 | 310 | 204 | 400 | 254 | 490 |